## Slide 1: Datacaptatie & visualisatie
Intro Node-RED

## Slide 2: Problem
Intro
  A lot of technologies for EMS (Energy Management Systems)
    Can one make a controller with current systems by exchanging data with each other?
  Load park
    Smappee EV charger
  3 battery storage
    Victron, SMA, Varta
  2 heatpump boilers
    Ariston, Vaillant
  1 air/Water heatpump
    Mitsubishi
  2 air/air heatpumps
    Kaysun, General
  2 smart resistor controllers
    GPC, My PV
  1 PV-installation
    Solaredge
  2 types sun collectors
  Accumulation heating
  classic household appliances
  # EMS systems

## Slide 3: Problem
  Every device has its own solution
    Example .. Battery storage Victron

## Slide 4: Intro Node-RED
Powerful tool for building IoT applications.
Visual programming : wiring together code blocks known as nodes.
Developed as an opensource project at IBM in 2013.
Useful for a range of applications.
Browser-based flow editor.
JavaScript functions can be created.
A built-in library
Built on Node.js (event-driven, non-blocking model)
Flows are stored in a JSON format.

## Slide 5: Node-RED and IoT
Rapid application devopment
Powerful and flexible
Flow-based programming => Messages representing events between nodes.
Not first choice for:
  Complex multi-function => complex to visualize
  Flow-based programming is cumbersome when handling loops
  Data analytics or build User Interface development
E.g.
  Use weather webrequest to control shutters
  Use fitbit to send email to activate the user
  Charge battery when electricity prices are low

## Slide 6: Intro Node-RED
Run at the edge of the network on low-cost hardware as well as in the cloud.

## Slide 7: Native installation on Windows
https://nodered.org/docs/getting-started/windows
Install Node.js => https://nodejs.org/en/
Check the Node.js installation
Install Node-RED
Installing Node-RED as a global module adds the command node-red to your system path. Execute the following at the command prompt:
npm install -g --unsafe-perm node-red

## Slide 8: Running on Windows
Once installed, the simple way to run Node-RED is to use the node-red command in a command prompt: If you have installed Node-RED as a global npm package, you can use the node-red command:
C:>node-red
This will output the Node-RED log to the terminal. You must keep the terminal open in order to keep Node-RED running. http://<ip-address>>:1880

## Slide 9: The Node-RED UI
The Node-RED UI consists of three main panes.
The node palette (left)
The flow canvas (centre)
The output pane (right)

## Slide 10: Node-RED nodes
Input Nodes (e.g. inject,connect to services)
Output Nodes (e.g. debug,tcp, email)
Processing Nodes (e.g. function)
Small grey square => input/output endpoints
Some nodes have a button to actuate or to enable/disable the node.
Small blue circle => flow needs to be updated

## Slide 11: Java script object
An object is a special data structure that lets you store values in key-values pairs.
A key (also called a property name) is usually a string.
A value can be anything: a number, string, array, function, or even another object.

## Slide 12: Messages
Node-RED nodes consume input messages and produce output messages.
Messages are JavaScript objects than contain a least a “payload” parameter.
Extend messages

## Slide 13: Message
Messages contain:
  payload
  topics
  internal identifier
Message is a JSON object

## Slide 14: First flow : Hello world
Demo:

## Slide 15: First flow : Info & Help

## Slide 16: First flow : Debug

## Slide 17: First flow => JSON object

## Slide 18: Node-RED => switch
Route messages based on their property values or sequence position.

## Slide 19: Exercise : switch with topics and JSON
Create an injection node with a few topics and JSON object in the payload.

## Slide 20: Exercise : switch with topics and JSON
Use a switch node to check the gender of the persons.
Use a switch node to divide up the age
Make a division between lectures and students

## Slide 21: Exercise : openweather
Create an account => we can use the openweather api
It can take an hour before your account is activated
https://openweathermap.org/api

## Slide 22: Sources
https://nodered.org/
https://nodered.org/docs/tutorials/
https://noderedguide.com/
https://dashboard.flowfuse.com/